## Slide 1: A Fast Routability- and Performance-Driven Droplet routing Simulation for Digital Microfluidic Biochips

## Slide 2: Outline
Introduction
Problem Formulation
Simulation Method
Experimental Results
Conclusion

## Slide 3: Digital MicroFluidic Biochip (DMFB)
Side view
Top view
Droplet
Bottom plate
Top plate
Ground electrode
Control electrodes (cells)
Hydrophobic insulation
Droplet
Spacing
High voltage to generate an electric field
The schematic view of a biochip
Reservoir/Dispensing port
Droplets
Control electrodes
Photodiode
2D microfluidic array
Droplet moving example

## Slide 4: Routing Constraints
Fluidic constraint
  For the correctness of droplet transportation
  No unexpected mixing among droplets of different nets
  Static and dynamic fluidic constraints
    Static constraint: > 1 or > 1
    Dynamic constraint: > 1 or > 1 or > 1 or > 1
Timing constraint
  Maximum transportation time of droplets
Minimum spacing
Static fluidic constraint
Dynamic fluidic constraint

## Slide 5: Outline
Introduction
Problem Formulation
Simulation Method
Experimental Results
Conclusion

## Slide 6: Droplet Routing on Digital Microfluidic Biochips
Input: A netlist of n droplets D = {d1, d2,…, dn}, the locations of blockages, and the timing constraint Tmax
Objective: Route all droplets from their source cells to their target cells while minimizing the number of unit cells and execution time for better fault tolerance and reliability
Constraint: Both fluidic and timing constraints are satisfied
2D microfluidic array
Droplets
Target
Fluidic constraint
Timing constraint

## Slide 7: Outline
Introduction
Problem Formulation
Experimental Results
Conclusion
Preferred Routing Tracks
Construction Stage
Routing Priority
Calculation Stage
Routing Compaction Stage
Simulation Method

## Slide 8: Preferred Routing Tracks Construction Stage
The goal of preferred routing tracks construction
  Reduce the design complexity for droplet routing
  Minimize the used cells for better fault-tolerance
  Minimum cost routing path

## Slide 9: Preferred Routing Tracks Construction Stage
Illustration
S1
S2
T1
T3
T2
d3
d1
d2
Moving vector analysis
Routing tracks construction

## Slide 10: Routing Priority Calculation Stage
Routing priority calculation
  Routing-resource-based equation that considers the congestion of routing region and interference with other nets globally
  Increase the routability for droplet routing with A-cells and concession control
Routing-resource-based equation (Entropy)
where ΔBEdi : the variant of entropy of each droplet
ΔQdi : the energy variant for this energy system
ESdi : the energy system for the droplet.

## Slide 11: Routing Priority Calculation Stage
S1
S2
T1
T3
T2
Route d2 to the A-cell of T2 by min-cost path
S3
Illustration
Routing priority calculation
=(36-((3+4)+4)+0)/36 = 25/36
=(24-((3)+0)+6)/24 = 27/24
=(36-((2+4)+6)+13)/36 = 37/36
Minimum cost path
d2
=(36-((2+4)+(6+6))+13)/36 = 31/36
d3
Concession Control
d1
Moving vector analysis
Routing tracks construction

## Slide 12: Routing Compaction Stage
Major goals:
  Transform the 2D routing into 3D routing considering the timing issue and maintain the original routing path
Optimal substructure:
  Optimally solution for a pair of droplets
  Find the solution by dynamic programming incrementally
X
Y
T

## Slide 13: Routing Compaction Stage
Illustration of dynamic programming
  Decode the 2D routing path into 1D moving string (u, d, l, r)
Incremental compaction strategy for routing path
P1
P2
P3
P4
Pn-1
Pn
compaction
compaction
compaction
…
compaction
compaction
S1
T1
S2
T2
MS1: rrrrrr
MS2: dddddrrrr
 |  | d | d | d | d | d | r | r | r | r
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
r | X | X | X | X | 4 | 5 | 6 | 7 | 8 | 9
r | X | X | X | X | X | 5 | 6 | 7 | 8 | 9
r | X | X | X | X | X | X | 6 | 7 | 8 | 9
r | X | X | X | X | X | X | X | 7 | 8 | 9
r | X | X | X | X | X | X | X | X | 8 | 9
r | X | X | X | X | X | X | X | X | X | 9
Compaction
d1
d2
d2
d2
d2
d2
d2
d2
d2
d2
d2
d1
d1
d1
d1
d1
d1
Used time = 9

## Slide 14: Outline
Introduction
Problem Formulation
Simulation Method
Experimental Results
Conclusion

## Slide 15: Experimental Result
Implemented our simulator in C++ language on a 2 GHz 64-bit Linux machine with 8GB memory
Compared with three state-of-the-art algorithms
  Prioritized A* search [K. Böhringer, TCAD’06]
  Network-Flow algorithm [Yuh et al, ICCAD’07]
  High-Performance algorithm [Cho and Pan, ISPD’08]
Tested on three benchmark suites
  Benchmark I [30] [Cho and Pan, ISPD’08]
  Benchmark II [10] [Self generated]
  Benchmark III [4] [Su and Chakrabarty, DAC’05]

## Slide 16: Experimental Result on Benchmark Suite I
Benchmark Suite I |  |  |  |  | Prioritized A* |  |  | Network-Flow |  |  | High-Performance |  |  | Our |  | 
Name | Size | #Net | Tmax | #Blk | #Fail | Tla | #Tcell | #Fail | Tla | #Tcell | #Fail | Tla | #Tcell | #Fail | Tla | #Tcell
Test1 | 12x12 | 12 | 100 | 23 | 0 | 37 | 66 | 2 | n/a | n/a | 0 | 100 | 67 | 0 | 39 | 73
Test2 | 12x12 | 12 | 100 | 25 | 4 | n/a | n/a | 7 | n/a | n/a | 1 | n/a | n/a | 0 | 47 | 65
Test3 | 12x12 | 12 | 100 | 28 | 4 | n/a | n/a | 6 | n/a | n/a | 1 | n/a | n/a | 0 | 41 | 58
Test4 | 12x12 | 12 | 100 | 31 | 3 | n/a | n/a | 5 | n/a | n/a | 0 | 70 | 64 | 0 | 38 | 71
Test5 | 16x16 | 16 | 100 | 39 | 0 | 28 | 108 | 2 | n/a | n/a | 0 | 78 | 118 | 0 | 40 | 100
Test6 | 16x16 | 16 | 100 | 30 | 0 | 43 | 116 | 0 | 44 | 132 | 0 | 55 | 119 | 0 | 47 | 98
Test7 | 16x16 | 16 | 100 | 52 | 0 | 33 | 104 | 3 | n/a | n/a | 0 | 89 | 113 | 0 | 44 | 93
Test8 | 16x16 | 16 | 100 | 54 | 2 | n/a | n/a | 0 | 47 | 129 | 0 | 41 | 94 | 0 | 49 | 96
Test9 | 16x16 | 16 | 100 | 72 | 4 | n/a | n/a | 3 | n/a | n/a | 1 | n/a | n/a | 0 | 49 | 91
Test10 | 16x16 | 16 | 100 | 67 | 4 | n/a | n/a | 2 | n/a | n/a | 0 | 77 | 110 | 0 | 51 | 94
Test11 | 24x24 | 24 | 100 | 106 | 0 | 62 | 252 | 0 | 100 | 264 | 0 | 47 | 249 | 0 | 56 | 228
Test12 | 24x24 | 24 | 100 | 104 | 3 | n/a | n/a | 0 | 80 | 242 | 0 | 52 | 219 | 0 | 62 | 231
Test13 | 24x24 | 24 | 100 | 137 | 0 | 60 | 241 | 2 | n/a | n/a | 0 | 52 | 247 | 0 | 62 | 221
Test14 | 24x24 | 24 | 100 | 143 | 3 | n/a | n/a | 2 | n/a | n/a | 0 | 57 | 234 | 0 | 64 | 219
Test15 | 24x24 | 24 | 100 | 173 | 0 | 63 | 246 | 0 | 74 | 233 | 0 | 83 | 230 | 0 | 64 | 227
Test16 | 24x24 | 24 | 100 | 185 | 4 | n/a | n/a | 3 | n/a | n/a | 0 | 63 | 223 | 0 | 58 | 220
Test17 | 32x32 | 32 | 100 | 315 | 9 | n/a | n/a | 2 | n/a | n/a | 0 | 68 | 394 | 0 | 77 | 409
Test18 | 32x32 | 32 | 100 | 327 | 4 | n/a | n/a | 0 | 88 | 408 | 0 | 91 | 403 | 0 | 73 | 385
Test19 | 32x32 | 32 | 100 | 357 | 0 | 70 | 402 | 2 | n/a | n/a | 0 | 90 | 371 | 0 | 81 | 367
Test20 | 32x32 | 32 | 100 | 363 | 3 | n/a | n/a | 0 | 91 | 382 | 0 | 99 | 393 | 0 | 78 | 360
Test21 | 32x32 | 32 | 100 | 364 | 8 | n/a | n/a | 2 | n/a | n/a | 0 | 76 | 389 | 0 | 85 | 370
Test22 | 32x32 | 32 | 100 | 363 | 5 | n/a | n/a | 4 | n/a | n/a | 0 | 85 | 393 | 0 | 73 | 369
Test23 | 48x48 | 48 | 100 | 645 | 6 | n/a | n/a | 0 | 100 | 681 | 0 | 78 | 738 | 0 | 75 | 709
Test24 | 48x48 | 48 | 100 | 653 | 8 | n/a | n/a | 0 | 99 | 737 | 0 | 94 | 807 | 0 | 82 | 717
Test25 | 48x48 | 48 | 100 | 763 | 5 | n/a | n/a | 0 | 100 | 729 | 0 | 91 | 792 | 0 | 87 | 698
Test26 | 48x48 | 48 | 100 | 770 | 3 | n/a | n/a | 0 | 99 | 709 | 0 | 88 | 798 | 0 | 84 | 691
Test27 | 48x48 | 48 | 100 | 857 | 4 | n/a | n/a | 0 | 100 | 770 | 0 | 99 | 762 | 0 | 92 | 739
Test28 | 48x48 | 48 | 100 | 864 | 5 | n/a | n/a | 4 | n/a | n/a | 0 | 99 | 808 | 0 | 87 | 726
Test29 | 48x48 | 48 | 100 | 1016 | 7 | n/a | n/a | 6 | n/a | n/a | 0 | 98 | 733 | 0 | 94 | 698
Test30 | 48x48 | 48 | 100 | 1017 | 8 | n/a | n/a | 4 | n/a | n/a | 0 | 88 | 751 | 0 | 92 | 701
Total |  |  |  |  | 106 |  |  | 61 |  |  | 3 |  |  | 0 |  | 
■ Size: Size of microfluidic array. ■ #Net: Number of droplets. ■ Tmax: Timing constraints. ■ #Blk: Number of blockage cells.
■ #Fail: Number of failed droplets. ■ Tla: latest arrival time among all droplets. ■ Tcell: Total number of cells used for routing.

## Slide 17: Experimental Result on Benchmark Suite I
Benchmark Suite I | High-Performance |  |  | Our |  | 
Name | Tla | #Tcell | CPU | Tla | #Tcell | CPU
Test1 | 100 | 67 | 0.11 | 39 | 73 | 0.08
Test4 | 70 | 64 | 0.13 | 38 | 71 | 0.09
Test5 | 78 | 118 | 0.47 | 40 | 100 | 0.21
Test6 | 55 | 119 | 0.25 | 47 | 98 | 0.24
Test7 | 89 | 113 | 0.47 | 44 | 93 | 0.37
Test8 | 41 | 94 | 0.27 | 49 | 96 | 0.19
Test10 | 77 | 110 | 0.49 | 51 | 94 | 0.64
Test11 | 47 | 249 | 0.55 | 56 | 228 | 0.81
Test12 | 52 | 219 | 1.59 | 62 | 231 | 0.91
Test13 | 52 | 247 | 1.52 | 62 | 221 | 0.98
Test14 | 57 | 234 | 3.03 | 64 | 219 | 2.82
Test15 | 83 | 230 | 1.42 | 64 | 227 | 2.08
Test16 | 63 | 223 | 0.95 | 58 | 220 | 1.74
Test17 | 68 | 394 | 2.42 | 77 | 409 | 3.85
Test18 | 91 | 403 | 1.32 | 73 | 385 | 0.91
Test19 | 90 | 371 | 1.33 | 81 | 367 | 0.78
Test20 | 99 | 393 | 5.76 | 78 | 360 | 3.71
Test21 | 76 | 389 | 11.22 | 85 | 370 | 4.31
Test22 | 85 | 393 | 5.13 | 73 | 369 | 4.18
Test23 | 78 | 738 | 3.59 | 75 | 709 | 5.84
Test24 | 94 | 807 | 3.66 | 82 | 717 | 5.78
Test25 | 91 | 792 | 4.30 | 87 | 698 | 6.91
Test26 | 88 | 798 | 3.71 | 84 | 691 | 4.11
Test27 | 99 | 762 | 6.26 | 92 | 739 | 5.41
Test28 | 99 | 808 | 4.31 | 87 | 726 | 5.97
Test29 | 98 | 733 | 36.47 | 94 | 698 | 9.72
Test30 | 88 | 751 | 29.72 | 92 | 701 | 8.14
Avg. | 1.21 | 1.10 | 1.40 | 1 | 1 | 1
■ Tla: latest arrival time among all droplets. ■ CPU: CPU time (sec)
■ Tcell: Total number of cells used for routing.

## Slide 18: Experimental Result on Benchmark Suite II
Comparison between the High-Performance routing algorithm and ours on Benchmark suite II
Benchmark Suite II |  |  |  |  | High-Performance |  |  | Our |  | 
Name | Size | #Net | Tmax | #Blk | #Fail | Tla | #Tcell | #Fail | Tla | #Tcell
Test a | 13x13 | 6 | 100 | 69 | 1 | n/a | n/a | 0 | 17 | 51
Test b | 13x13 | 5 | 100 | 53 | 2 | n/a | n/a | 0 | 13 | 33
Test c | 16x16 | 7 | 100 | 95 | 0 | 29 | 74 | 0 | 24 | 61
Test d | 16x16 | 9 | 100 | 133 | 2 | n/a | n/a | 0 | 27 | 87
Test e | 24x24 | 10 | 100 | 173 | 0 | 38 | 170 | 0 | 38 | 128
Test f | 24x24 | 12 | 100 | 215 | 3 | n/a | n/a | 0 | 45 | 129
Test g | 32x32 | 6 | 100 | 440 | 2 | n/a | n/a | 0 | 39 | 121
Test h | 32x32 | 8 | 100 | 485 | 1 | n/a | n/a | 0 | 39 | 88
Test I | 48x48 | 12 | 100 | 1013 | 3 | n/a | n/a | 0 | 85 | 197
Test j | 48x48 | 20 | 100 | 1079 | 0 | 86 | 637 | 0 | 83 | 459
Total |  |  |  |  | 14 |  |  | 0 |  | 
■ Size: Size of microfluidic array. ■ #Net: Number of droplets. ■ Tmax: Timing constraints.
■ #Blk: Number of blockage cells. ■ #Fail: Number of failed droplets.
■ Tla: latest arrival time among all droplets. ■ Tcell: Total number of cells used for routing.

## Slide 19: Experimental Result on Benchmark Suite III
Comparison of the Network-Flow-Based algorithm, the High-Performance routing algorithm and ours on Benchmark suite III
Benchmark Suite III |  |  |  |  |  | Network-Flow | High-Performance | Our
Name | Size | #Sub. | #Net | # Tmax | #Dmax | #Tcell | #Tcell | #Tcell
in-vitro_1 | 16 x 16 | 11 | 28 | 20 | 5 | 237 | 258 | 231
in-vitro_2 | 14 x 14 | 15 | 35 | 20 | 6 | 236 | 246 | 229
protein_1 | 21 x 21 | 64 | 181 | 20 | 6 | 1618 | 1688 | 1588
protein_2 | 13 x 13 | 78 | 178 | 20 | 6 | 939 | 963 | 923
Avg. |  |  |  |  |  | 1.023 | 1.074 | 1.000
■ Size: Size of microfluidic array. ■ #Sub: Number of subproblems. ■ #Net: Number of droplets.
■ Tmax: Timing constraints. ■ #Dmax: Maximum number of droplets among subproblems.
■ Tcell: Total number of cells used for routing.

## Slide 20: Outline
Introduction
Problem Formulation
Simulation Method
Experimental Results
Conclusion

## Slide 21: Conclusion
We proposed a fast routability- and performance-driven droplet simulator for DMFBs
Experimental results shown that our simulator can achieve better timing result (Tla) and fault tolerance (#Tcell) compared with the best known results
Experimental results demonstrated that our simulator achieves 100% routing completion for all test cases in three Benchmark Suites while the previous algorithms are not

## Slide 22: DEMO
UI Demonstration

## Slide 23
Thank You for
Your Attention!