## Slide 1
UI-Timer: An Ultra-Fast Clock Network Pessimism Removal Algorithm
Tsung-Wei Huang, Pei-Ci Wu, and Martin D. F. Wong
Department of Electrical and Computer Engineering (ECE)
University of Illinois at Urbana-Champaign (UIUC), IL, USA
2014 IEEE/ACM International Conference on Computer-Aided Design
Notes: ECE Main Slide

## Slide 2
Outline
Introduction
  Static timing analysis (STA)
  Importance of clock network pessimism removal
Problem formulation
  2014 TAU timing analysis contest
Experimental result
Conclusion

## Slide 3
Static Timing Analysis (STA)
Static Timing analysis
  Verify the expected timing characteristics of integrated circuits
  Keep track of path slacks and identify the critical path with negative slack
Increasing significance of variance
  On-chip variation such as temperature change and voltage drop
  Perform dual-mode (min-max) conservative or pessimistic analysis
  Degrades the quality of signoff timing report

## Slide 4
Timing Test and Verification of Setup/Hold Check
Sequential timing test
  Setup time check
    “Latest” arrival time (at) v.s. “Earliest” required arrival time (rat)
  Hold time check
    “Earliest” arrival time (at) v.s. “Latest” required arrival time (rat)
Passing (positive slack)
Earliest rat
(hold test)
time
Latest rat
(setup test)
Hold violation 
No violation 
Setup violation 
Failing
Failing

## Slide 5
Clock Network (Common Path) Pessimism
Common path pessimism (CPP)
  Simultaneous min-max variation along the common clock paths
    Impossible in reality
  Unnecessary pessimism is included into the path slack
    Test marking failing might be passing in actuality

## Slide 6
Example – Data Path Slack with CPPR Off
Pre common-path-pessimism-removal (CPPR) slack
  Data path 1: ((120+(20+10+10))-30) – (25+30+40+50) = -15 (critical)
  Data path 2: ((120+(20+10+10))-30) –(25+45+40+50) = -30 (critical)

## Slide 7
Example – Data Path Slack with CPPR On
Post common-path-pessimism-removal (CPPR) slack
  Data path 1: ((120+(20+10+10))-30) – (25+30+40+50)+5 = -10 (critical)
  Data path 2: ((120+(20+10+10))-30) –(25+45+40+50)+40 = 10
+5
+40
CPP1
CPP 2

## Slide 8
Impact of Clock Network Pessimism – (I)

## Slide 9
Importance of Clock Network Pessimism Removal
Over-pessimistic timing report
  Report failure paths but in actuality passing
  Mislead designer into an inaccurate timing result
  Decrease the productivity and legality of turnaround
  Most critical pre-CPPR path(s) could be positive post-CPPR path(s)
  Mislead CAD tools and result in wastage of optimization efforts
  Leaving performance on Table
Increasing significance in deep sub-micro era
  Industry people seek novel ideas for CPPR algorithm
  2014 TAU CAD Contest on CPPR
    Worldwide teams participated in the contest
    1st place winner – UI-Timer

## Slide 10
Problem Formulation
Input file
  Delay file for circuit topology and tests
  Timing file for assertion and clock properties
Goal
  Identify the top k critical paths with CPPR (i.e., post-CPPR critical paths)

## Slide 11
Algorithm - Overview
Step 1: look-up-table preprocessing
  Tabulate the common path for quick pessimism lookup
Step 2: pessimism-free graph formulation
  Facilitate the search on true post-CPPR slack
Step 3: path extraction
  Search the top k critical paths in the pessimism-free graph

## Slide 12
Algorithm – Step 1: Lookup Table Preprocessing
Pessimism incurs on a clock re-converging node
  Equivalently finding the lowest common ancestor (LCA) in the clock tree
  Range minimum query with dynamic programming
  O(nlogn) preprocessing and O(1) per LCA query

## Slide 13
Algorithm – Step 2: Pessimism-Free Graph Formulation
Pessimism-free graph formulation
  Isolate the constant part of numerical slack value
    Offset weight for required arrival time and common-path pessimism
  Facilitate the search
    The cost of path is equivalent to post-CPPR slack
Pessimism-free graph
slackhold = atdearly – rattearly + CPPds
slacksetup = rattlate – atdlate + CPPds
Constant per test
Constant per test
Wholdoffset = – rattearly + CPPds
Wsetupoffset = rattlate + CPPds

## Slide 14
Algorithm – Step 3: Extraction of Top k Critical Paths (I)
O(N) explicit path representation
  Path = <v1, v2, v3, … vn> or <e1, e2, e3, … em>
O(1) implicit path representation
  Path = <ei>
Referencing to the shortest path tree
=> edge as “Deviation”

## Slide 15
Algorithm – Step 3: Extraction of Top k Critical Paths (II)
Deviation cost
  dist[v]: the shortest path distance from node v to the target
  devi[e]: the distance loss by deviating on the edge “e”
    head[e] = v, tail[e] = u
    devi[e] = dist[v] + we – dist[u]
Intuition: distance loss
v
u
devi[e] = dist[v] + we – dist[u]
(always non-negative!)
e

## Slide 16
Algorithm – Step 3: Extraction of Top k Critical Paths (III)
Spur procedure
  Growth of the prefix tree (neighboring expansion)
  Take a path p and generate all other paths deviated from this path p
  Mark the deviation cost

## Slide 17
Algorithm – Step 3: Extraction of Top k Critical Paths (IV)
Suffix Tree
  Shortest path tree rooted at destination node (static)
Prefix Tree
  Tree order of non-suffix-tree nodes (path deviation)

## Slide 18
Algorithm – Step 3: Extraction of Top k Critical Paths (V)
Priority search
  Pick up a prefix-tree node with the minimum cost
  Recover the path and mark it as the current most critical path
  Perform the spur operation on this path
  Repeat until the top k critical paths have been found
Optimality
  Analogy to typical graph search
Iterative expansion from the frontier node with the least cost
Spur

## Slide 19
Algorithm – Exemplification (I)
Build the suffix tree
  Find the shortest distances of all nodes to the target

## Slide 20
Algorithm – Exemplification (II)
Perform the spur procedure
  Spur along the first critical path (k=1)

## Slide 21
Algorithm – Exemplification (III)
Perform the spur procedure
  Spur along the second critical path (k=2)

## Slide 22
Algorithm – Exemplification (IV)
Perform the spur procedure
  Spur along the third critical path (k=3)

## Slide 23
Algorithm – Exemplification (V)
Perform the spur procedure
  Spur along the forth critical path (k=4)

## Slide 24
Algorithm – Exemplification (VI)
Perform the spur procedure
  Spur along the sixth critical path (k=6)

## Slide 25
Experimental Results – (I)
Environment
  C++ implementation
  Ubuntu 10.4 Linux system
  4 Intel i7 cores and 8GB memory
Benchmark from TAU 2014 Contest
  Sequential circuits
  Open core circuits
  Combo series
Baseline timers
  LightSpeed (2nd place timer)
  iTimerC (3rd place timer)
Sequential circuits
(6-42 tests)
Open core
(380-50K tests)
Combo series
(8K-110K tests)

## Slide 26
Experimental Results – (II)

## Slide 27
Experimental Results – (III)
Circuits
  tv80
  systemcaes
Runtime plot
  1st: UI-Timer
  2nd: LightSpeed
  3rd: iTimerC
Accuracy plot
  1st: UI-Timer
  2nd: iTimerC
  3rd: LightSpeed

## Slide 28
Conclusion
A fast and exact algorithm for CPPR
  Lookup table for clock network pessimism
  Efficient data structure for path representation
Evaluation
  1st place timer in TAU 2014 CAD contest for timing analysis
  Handled million-scale graph within 1 hr
    Other timers either crashed or ran over 3 hrs
Future work
  Incremental timing and CPPR
  Distributed computing for path-based analysis