## Slide 1
UI-Route: An Ultra-Fast Incremental Maze Routing Algorithm
Tsung-Wei Huang, Pei-Ci Wu, and Martin D. F. Wong
Department of Electrical and Computer Engineering (ECE)
University of Illinois at Urbana-Champaign (UIUC), IL, USA
2014 IEEE/ACM System Level Interconnect Prediction Workshop
Notes: ECE Main Slide

## Slide 2
Outline
Introduction
Problem formulation
Algorithm
Experimental result
Remark

## Slide 3
Introduction
Maze routing
  Trace a shortest connection between two specified grid points
  A primary problem in many science/engineering disciplines
Electronic-design-automation (EDA) applications
  IC routing (e.g., global/detailed routing)
  PCB routing (e.g., escape routing)
  FPGA routing (e.g., negotiation-based routing)
Source
Target
Blocked node
Unblocked node

## Slide 4
Existing Approaches
Breadth-first-propagation (BFP) style
  Maintain the optimal substructure of shortest path
  Search from nodes having shortest routes already
  Optimal and complete but slow
  Lee’s algorithm, A* search, etc.
Depth-first-line-search (DFL) style
  Neglect the optimal substructure of shortest path
  Search in greedy manner
  Suboptimal and incomplete but fast
  Hightower’s algorithm, Soukup’s algorithm, etc.

## Slide 5
Motivation
Pros and cons between BFP and DFL variants
  BFP variants are optimal and complete but usually slow
  DFL variants trade optimality and completeness for speedup
A common shortcoming of existing approaches
  Focus on a single route query at one time
  However, practical applications require incremental processing
    Route queries
    Graph updates
  Deal with each route query independently
    Overlapped and redundant search efforts 
    No reutilization of search knowledge 
    Runtime and speedup bottleneck 
  Unknown acceleration challenges

## Slide 6
Problem Formulation
Incremental maze routing problem
  Solve route queries subject to graph updates
  Query (S, T): Find the shortest connection between S and T
  Update (x, y): Block/Unblock the grid node at (x, y)
Goal
  Optimality
  Completeness
  Speedup
*Optimality: the route is the shortest
*Completeness: find a route if exists

## Slide 7
Algorithm – Breaking the Equivalent Routes
Definition 1: Given two distinct grid nodes g1 and g2, two routes r1 from g1 and r2 from g2 are equivalent, if they have identical route lengths
Definition 2: Given two distinct grid nodes g1 and g2, g2 is a breaking node from g1 if g2 has a neighbor n such that g2 is a must intermediate on the optimal route from g1 to n
B is a breaking node from the left red dot

## Slide 8
Algorithm – Horizontal Breaking (I)
Horizontal Breaking: Given a node g and its present direction d in horizontal, the node gH is a horizontal breaking node from g if gH is reachable from g by heading along direction d and is the nearest such node to satisfy one of the following conditions
  gH is blocked or out of boundary
  gH has a vertically adjacent neighbor whose optimal route from g must pass gH
B is a horizontal breaking node from S
Concept behind
  A dimensional rephrase of definition 2
  Online definition with respect to present search direction

## Slide 9
Algorithm – Horizontal Breaking (II)
Uniform grid graph
  Totally six cases of horizontal breaking nodes from either direction
Table lookup
  Successor table maps grid nodes to horizontal breaking nodes
  Satellite table keeps track of the furthest mapping
Both tables can be filled out
in recursive manner!

## Slide 10
Algorithm – Vertical Breaking
Vertical Breaking: Given a node g and its present direction d in vertical, the node gV is a vertical breaking node from g if gV is reachable from g and is the nearest such node to satisfy the following condition
  At least a horizontal breaking node of cases 3-6 (blocked nodes and out-of-boundary nodes) exists from gV
gV is a vertical breaking node from S
Concept behind
  Constitute the definition 2 with horizontal breaking nodes
  Online definition with respect to present search direction

## Slide 11
Algorithm – Route Query
Research route over horizontal/vertical breaking nodes
  Each horizontal expansion traces the horizontal breaking nodes
  Each vertical expansion traces the vertical breaking nodes
  Update the table if necessary
  Framed in generic A* search – Optimality and Completeness

## Slide 12
Algorithm – Graph Update
Graph update can be quickly reflected on satellite table
  Satellite table states one-to-one mapping
  Shrink the satellite field of the horizontal breaking
Graph update operations
  Block a grid node
    Case 1: Consistent
    Case 2: Vanish
    Case 3: Cutoff
  Unblock a grid node
    Case 1: Consistent
    Case 2: Vanish
    Case 3: Cutoff
Shrink the satellite field

## Slide 13
Algorithm – Graph Update
Graph update example
  Examine the three cases per grid update
  Examination takes constant time
  Shrink the satellite field if necessary
  Incrementally fill in the tables in the next route query

## Slide 14
Experimental Results – (I)
UI-Route is implemented in C++ language on a 2.67GHz 64-bit Linux machine with 8GB memory
Benchmarks from ISPD placement contests
  Scale the layout into a grid graph with maximum dimension being 2048
  Randomly generate 1000 route queries subject to graph updates
  Simulate the rip-up and reroute procedure
Baseline
  Lee’s algorithm
  A* search algorithm
  Soukup’s algorithm

## Slide 15
Experimental Results – (II)
Performance comparison
  Only measure the runtime taken on search
  Storage initialization is not included

## Slide 16
Experimental Results – (III)
Runtime value including storage initialization
  Naïve initialization prior to each search
  Clear the all data structure (e.g., queue, distance table, etc.)

## Slide 17
Experimental Results – (IV)
Snapshot 1
  Lee’s algorithm
  A* search
  UI-Route
Snapshot 2
  A* search
  Soukup’s algorithm
  UI-Route
A* search has x0.4 speedup
UI-Route has x6.0 speedup
Soukup has x1.5 speedup
UI-Route has x9.0 speedup

## Slide 18
Concluding Remark
An incremental maze routing algorithm is introduced
  Incremental processing of route queries and graph updates
  Reutilization of search knowledge among routing queries
  Reduce overlapped search efforts for speedup
  Ease of coding, simple data structure, orthogonal to many routers
Take-home message
  UI-Route is superior when the grid graph is highly sparse
  Clever data structure matters (binary heap v.s. array heap)
  Non-algorithmic speedup technique contributes to further speedup
Future work
  Apply to weighted grid graph